## Slide 1: VHDL 5 FINITE STATE MACHINES (FSM)
Some pictures are obtained from
FPGA Express VHDL Reference Manual, it is accessible from the machines in the lab at /programs/Xilinx foundation series/VDHL reference manual
/programs/Xilinx foundation series/foundation project manager/foundation help content/XVDHL compiler help pages

## Slide 2: Contents: You will learn
Finite state machines FSMs
Feedback using signals or variables
Use of clocks, processes to make FSMs
Different types of Finite State Machines
  Moore
  Mealy

## Slide 3: Finite State machines FSM
A system jumps from one state to the next within a pool of finite states upon clock edges and input transitions. (traffic light, digital watch, CPU).

## Slide 4: TO WRITE CLOCK EDGES
Using if-then-else

## Slide 5: Clock edges: Use of “if Statements” or “Wait until” to represent Flip-flops
Test for edge of a signal.
  if SIGNAL’event and SIGNAL = ’1’ -- rising edge
  if SIGNAL’event and SIGNAL = ’0’ -- falling edge
Or
In a wait statement, edge can also be
  wait until CLK = ’1’; -- rising edge triggered
  wait until CLK = ’0’;--falling edge triggered

## Slide 6: Use of ‘Wait’ and ‘If’ for clock edge detection
Clock edge detection
Synchronous processes
Asynchronous processes
clock edge detection:
Use ‘Wait’ or ‘IF’
clock edge detection:
Use ‘IF’ only

## Slide 7: Clock edges: compare wait and if Statements
IEEE VHDL requires that a process with a wait statement must not have a sensitivity list.
In general, the following guidelines apply:
  Synchronous processes (processes that compute values only on clock edges) must be sensitive to the clock signal. Use wait-until or if.
  When Wait is used: The first statement must be wait until, E.g.
    Process  no sensitivity list, implies there is one clock as input
    Begin
    Wait until clock =‘1’
  Asynchronous processes (processes that compute values on clock edges and when asynchronous conditions are TRUE) must be sensitive to the clock signal (if any), and to inputs that affect asynchronous behavior. Use “if” only.
    E.g. Process (clock, input_a, input_b…)

## Slide 8: THE FEEDBACK CONCEPT
For making FSM

## Slide 9: The feedback concept
So far you learned logic with feed forward paths only.
Now, you will see feedback paths.
The first step of the making a state machine

## Slide 10: Feedback 1 -- direct feedback
library IEEE;--(ok Vivado 2014.4 & ISE)
use IEEE.STD_LOGIC_1164.ALL;
entity some_entity is
port (a, clk, reset: in std_logic;
c : buffer std_logic); -- or use inout
end some_entity;
-------------------------------------------
architecture example of some_entity is
begin
process(clk,reset)
begin
if reset = '1' then c <= '0';
elsif rising_edge(clk)
then c<= not(a and c);
end if;
end process;
end example; -- synthesized ok
a
c
clk
reset
D
Q
Clock
reset
b
If C is an IO pin connected outside, it
must have type inout or buffer

## Slide 11: Concentrate on the following lines of Feedback 1 Use of signals in a clocked process
13) elsif rising_edge(clk)
14) then c<= not(a and c);
****************Note ***********
  Current not(a and c) affects next b

## Slide 12: Worksheet 5.1
Initially c=0
Draw c
a
c
clk
reset
D
Q
Clock
reset
b
Clock
Reset
a
c

## Slide 13: Feedback 2 -- using signals
library IEEE;--(ok Vivado 2014.4 & ISE)
use IEEE.STD_LOGIC_1164.ALL;
entity some_entity is
port (a, clk, reset: in std_logic;
c : inout std_logic); -- or use inout
end some_entity;
-------------------------------------------
architecture example of some_entity is
signal b: std_logic; -- internal signal b is global,
begin
process(clk,reset)
begin
if reset = '1' then c <= '0';
elsif rising_edge(clk)
then b<= not(a and c);
c <= b;
end if;
end process;
end example; -- synthesized ok
a
c
clk
reset
D
q
Clock
reset
b1
If C is an IO pin connected outside, it
must have type inout or buffer
D q
b2

## Slide 14: Concentrate on the following lines of feedback 2 Use of signals in a clocked process
15) then b<= not(a and c);
16) c <= b;
****************Note ***********
  Current {not (a and c)} affects next b
  Previous (before 8 is executed) b affects c
  The two b’s in the process have different states

## Slide 15: Exercise 5.2
Initially c=0,b1=1,b2=1
Draw b2,c
Clock
reset
a
b1
b2
c
reset
a
c
clk
D
q
Clock
reset
b1
D q
b2

## Slide 16: Feedback 3 -- using variables
library IEEE;--(ok Vivado 2014.4 & ISE)
use IEEE.STD_LOGIC_1164.ALL;
entity some_entity is
port (a, clk, reset: in std_logic;
c : buffer std_logic); -- or use inout
end some_entity;
-------------------------------------------
architecture example of some_entity is
begin
Process -- no sensitivity list for 'wait unit'
variable v: std_logic; --v is local
begin
wait until clk = '1';
if reset = '1' then v := '0';
else v := not (a and c);
c <= v;
end if;
end process;
c
clk
reset
D
Q
Clock
reset
v
If C is an IO pin connected outside, it
must have type inout or buffer
a

## Slide 17: Concentrate on the following lines of feedback 3 Use of signals in a clocked process
15) else v := not (a and c);
16) c <= v;
****************Note ***********
  Current not(a and c) affects next variable v
  The new variable (after line6 is executed) v affects c
  This is the main difference between signal and variable in a clocked process
    Signals do not change immediately
    Variables change immediately

## Slide 18: Exercise 5.3
Initially c=0
Draw c
Clock
Reset
a
c
c
clk
reset
D
Q
Clock
reset
v
a

## Slide 19: Use of modes : inout and buffer in feedback
Buffer can be read back
inout allows for internal feedback, it can also read external signals.
in
out
out
in
in
Inout
buffer

## Slide 20: Important: Feedback using signals and variables will give different results.
Variable: A variable in a process can update many times.
Signal:
  “<= ” can be treated as a flip-flop
  (left side of “<= ” is output, right side of “<= ” is input) , it only updates once when the process executes at the triggering clock edge.
  When a signal is assigned to different values by different statements in a process, only the last statement is effective.

## Slide 21: Inside a process
Signals in a process:
  Combination process=the process has no clock edge detection: only the last assignment statement for that particular signal counts, the assignment is a combinational logic circuit.
  Clocked process=the process has clock edge detection (e.g. if rising_edge(clk) )
    Signal assignment before clock edge detection: same as combination processes (same as above).
    Assignment after clock edge detection: the assignment is a flip-flop.
Variables in processes (only live in processes anyway): when all signals are stable, then use your old programming common sense. Assignments take effect immediately.
The Trick!!

## Slide 22: EXAMPLE TO SHOW
The difference between signal and variables in feedback processes

## Slide 23
process( S1, S2 )
variable V1, V2: BIT;
begin
V1 := ’1’; -- This sets the value of V1
V2 := ’1’; -- This sets the value of V2
S1 <= ’1’; -- This assignment is the driver for S1
S2 <= ’1’; -- This has no effect because of the
-- assignment later in this process
S_OUT(1) <= V1; -- Assigns ’1’, the value assigned above
S_OUT(2) <= V2; -- Assigns ’1’, the value assigned above
S_OUT(3) <= S1; -- Assigns ’1’, the value assigned above
S_OUT(4) <= S2; -- Assigns ’0’, the value assigned below
V1 := ’0’; -- This sets the new value of V1
V2 := ’0’; -- This sets the new value of V2
S2 <= ’0’; -- This assignment overrides the
-- previous one since it is the last assignment to this signal here
S_OUT(5) <= V1; -- Assigns ’0’, the value assigned above
S_OUT(6) <= V2; -- Assigns ’0’, the value assigned above
S_OUT(7) <= S1; -- Assigns ’1’, the value assigned above
S_OUT(8) <= S2; -- Assigns ’0’, the value assigned above
end process;
(page 6-9 xilinx foundation4.2 vhdl reference)
signal S1, S2: BIT; --
signal S_OUT: BIT_VECTOR(1 to 8);

## Slide 24
(See VHDL reference manual version : chapter 6 [sequential statements]: variable/signal assignment statements.)
signal S1, S2: BIT;
signal S_OUT: BIT_VECTOR(1 to 8);
. . .
process( S1, S2 )
variable V1, V2: BIT;
begin
V1 := ’1’; -- This sets the value of V1
V2 := ’1’; -- This sets the value of V2
S1 <= ’1’; -- This assignment is driver for S1
S2 <= ’1’; -- This has no effect because of the
-- assignment later in this process

## Slide 25
S_OUT(1) <= V1; -- is ’1’, the value assigned above
S_OUT(2) <= V2; -- is ’1’, the value assigned above
S_OUT(3) <= S1; -- is ’1’, the value assigned above
S_OUT(4) <= S2; -- is ’0’, the value assigned below
V1 := ’0’; -- This sets the new value of V1
V2 := ’0’; -- This sets the new value of V2
S2 <= ’0’; -- This assignment overrides the
-- previous one since it is the last
-- assignment to this signal in this
-- process

## Slide 26
S_OUT(5) <= V1; -- is ’0’, the value assigned above
S_OUT(6) <= V2; -- is ’0’, the value assigned above
S_OUT(7) <= S1; -- is ’1’, the value assigned above
S_OUT(8) <= S2; -- is ’0’, the value assigned above
end process;

## Slide 27: Examples: signals and variables in process( ) See Roth p.66
Process --a variable can change value many times in a process
variable v1: integer :=1; --initialized to1
variable v2: integer :=2; --initialized to 2
variable v3: integer :=3;--iniltialized to 3
begin wait on trigger;
--find results after clock edge--------------- t1 t2 t3 t4
v1:=v2+v3; -- after t1, now v1 = 2+3=5 5 10 20 40
v2:=v1; -- after t1, now v2=5 5 10 20 40
v3:=v2; -- after t1, now v3=5 5 10 20 40
sum<=v1+v2+v3; 15 30 60 120
-- so sum=5+5+5=15 after the first trigger clock edge.
end process
Variables case

## Slide 28
Exercise 5.4:Architecture sig_arc of example is
signal s1: integer:=1;
signal s2: integer:=2;
signal s3: integer:=3;
begin -- t1 is just after the first clk edge, etc
process begin wait on clk;-- t1 t2 t3 t4
s1<=s2+s3; -- s1=
s2<=s1; -- s2=
s3<=s2; -- s3=
sum<=s1+s2+s3;--sum=
end process
end
__ __ __ __
__ __ __ __
__ __ __ __
__ __ __ __
Signal case

## Slide 29
library IEEE; -- successfully compiled and tested;--(syn. ok Vivado 2014.4 )
use IEEE.STD_LOGIC_1164.all; -- so use reset to set them to init values
use IEEE.std_logic_arith.all;
use IEEE.std_logic_unsigned.all;
entity some_entity is
port ( clk : in STD_LOGIC;
reset : in STD_LOGIC;
sportsum: out integer);
end some_entity;
Architecture sig_arc of some_entity is
signal t1, t2, t3 : integer; -- In Xilinx, ini. Signals cannot be done
begin -- t1 is just after the first clk, etc
--with clk, without clk, with s1234, in sen. list or not
process(clk,reset) -- clocked process, syn. input can be in or not in the sensitivity list
-- begin wait on clk;-- t1 t2 t3 t4
begin if reset = '1’ then -- use reset to set them to init values
t1 <= 1;
t2 <= 2;
t3 <= 3;
sportsum <= 0;
elsif clk='1' and clk'event then
t1<=t2+t3; -- s1=
t2<=t1; --s2=
t3<=t2; --s3=
sportsum <= t1+t2+t3; -- sum= 6, 8, 9, 14 after each clock edge
end if; end process;
end sig_arc;

## Slide 30
Exercise 5.5: architecture example of some_entity is
signal con1: std_logic; -- b is global, bit is a VHDL type
begin
process(clk,reset)
variable v1: std_logic;
begin
if reset = '1' then out1 <= '0'; out2<='0'; out3<='0';con1<='1';
elsif rising_edge(clk) then
---case 1 ----- direct feedback
out1<= not(in1 and out1); -- out1 is immediate
---case 2 ----- feedback using signal
con1<= not(in1 and out2);
out2<= con1; -- out2 is delayed hence lower frequency
---case 3 ----- feedback using variable
v1:=not(in1 and out3); -- out3 is immediate
out3 <= v1;
end if; end process; end example; -- synthesized
Plot result.
Try this in lab and explain the result

## Slide 31: Worksheet 5.5
Clock
Reset
Out1
Out2
Out3
Con1

## Slide 32: Types of FSM Finite State machines -Study FSMs with inputs other than the clock
FSM
Moore machine
Mealy machine

## Slide 33: State machine designs, 2 types
A Moore machine’s outputs are a function of the present state only.
A Mealy machine’s outputs are a function of the present-state and present-inputs.

## Slide 34: Moore machine, an example F1 is B<= not (A and C) F2 is D<= not C
Output is a function of the state registers.
The simplest Moore machine use only one process , see next page
Nand
not
D type
Flip-Flop (FF)

## Slide 35: Moore machine example 1 architecture moore2_arch of system is 2 signal C: bit; -- global, can be seen by different
3 begin
4-- since D is purely for output, no feedback read
5 -- requirement, so it has the type out
6 D <= not C; -- F2 = combination logic
7--
8 process -- sequential logic
9 begin
10 wait until clock;
11 C <= not (A and C); --F1 = combination logic
12 end process;
13 end moore2_arch;
process :F1

## Slide 36
library IEEE; -- Moore2 example ,-- synthesized ok. (ISE % Vivado 2014.4)
use IEEE.std_logic_1164.all;
entity some_entity is ----------------------------------------------
port (
clock: in std_logic;
A,reset: in std_logic;
D: inout std_logic -- no need to use inout or buffer type, since there is no need to read.
);
end some_entity;
architecture moore2_arch of some_entity is
signal B,C: std_logic; ----------------------------------------------
begin
process (C) -- combinational logic
begin
D <= not C; -- F2 = combination logic
end process;
process(clock,reset) -- sequential logic
begin
if reset = '1' then c <= '0';
elsif rising_edge(clock)then
C <= not (A and C); --F1 = combination logic
end if;
end process;
end moore2_arch;

## Slide 37: Moore machine using 2 processes
It is more flexible and easier to design.
You can make it formal that F1 is an operation (a concurrent line of code) and
F2 is another operation (a process)

## Slide 38: Exercise 5.6 ,exercise on Moore machine, draw c (init. c=0)
clock
C=/D when A=1
C=/D when A=0
Nand
not
D type
FF

## Slide 39: Mealy machine
A Mealy machine’s outputs are a function of the present state and the inputs.

## Slide 40: Mealy machine, an example
A Mealy Machine can use two processes, since its timing is a function of both the clock and data inputs.
F1 is C <= not(A or C); F2 is D <= (A or C)
In the diagram we can say that B is the current output of not( A and C), but B does not need to exist, writing C <= not(A or C) is enough
F1 is B <= not(A or C); F2 is D <= (A or C)
Nor
or
D Q
D-Flip-Flop

## Slide 41: Mealy machine outputs are a function of the present state and the inputs.
library IEEE; -- Mealy example ,-- synthesized ok. ( Vivado 2014.4)
use IEEE.std_logic_1164.all;
entity some_entity is ----------------------------------------------
port (
clock: in std_logic;
A,reset: in std_logic;
D: inout std_logic -- no need to use inout or buffer type, since there is no need to read.
);
end some_entity;
architecture mealy_arch of some_entity is
signal C: std_logic; ----------------------------------------------
begin
process (A,C) -- combinational logic process
begin
D <= (A or C);--F2 = combination logic
end process;
---------------------------------------------
process(clock,reset) -- sequential logic
begin
if reset = '1' then c <= '0';
elsif rising_edge(clock)then
C <=not(A or C);--F1 = combination logic
end if;
end process;
end mealy_arch;
Operation :F1
Operation :F2

## Slide 42: Exercise 5.7: on Mealy machine, Plot C,D (init. c=0)
F1 is B <= not(A or C); F2 is D <= (A or C)
A
C
D
clock
Nor
or
D Q
D-Flip-Flop

## Slide 43: Quick revision
You should know
  How to write a clock edge detector
  Feedback theory and implementation
  Design Moore and Mealy machine
  Use of signal and variables and understand their differences